## Slide 1
STATIC ROBO HMI TEST JIG
Professional research report: effectiveness, versatility, operating cost, and strategic advantages versus a robotic hand
Core thesis
For fixed HMI validation, a purpose-built static fixture provides higher repeatability, lower total cost, easier service, and better integration of camera feedback and cloud data than a dexterous robotic hand.
HMI DISPLAY
CAM
Prepared for HMI validation, production test, and in-vehicle endurance use cases

## Slide 2
DECISION CONTEXT
Executive summary
Static jig
recommended platform
Purpose-built for repeatable HMI actuation and verification
Lower TCO
ownership profile
Commodity components, easier repairs, less calibration
Portable
deployment profile
Compact enough for bench, field, and vehicle cabin testing
Higher traceability
data quality
Camera + electrical + cloud records in one sequence
Question
Static HMI Test Jig
Robotic Hand
What is optimized?
Known HMI test points, visual verification, repeatability
General human-like manipulation
Best operating environment
Production, validation lab, field diagnostics, in-vehicle endurance
Research lab, manipulation research, unknown objects
Main advantage
Lower cost, high repeatability, modular scaling
High dexterity for variable manipulation tasks
Main weakness
Needs fixture adaptation for each HMI family
High cost, high complexity, more maintenance
Recommendation
Use as primary HMI validation platform
Use only if human-like manipulation is truly required
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
2

## Slide 3
ENGINEERING FIT
Fit-for-purpose comparison: HMI validation needs measurement, not human imitation
HMI validation requirement
A test system must press/touch/turn known controls, verify screen response, record data, and repeat the sequence hundreds or thousands of times with stable geometry.
Robotic hand mismatch
A robotic hand spends cost and complexity on dexterity, grasping, joint coordination, and human-like motion that usually does not improve HMI pass/fail confidence.
contact location
force / dwell time
screen verification
data traceability
service uptime
Static jig aligns directly with the HMI test stack
finger kinematics
grip planning
joint calibration
slip detection
arm safety envelope
Robotic hand adds capabilities that are not central to pass/fail HMI testing
Cost and risk should be assigned to the test requirement, not to human-like appearance.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
3

## Slide 4
REFERENCE ARCHITECTURE
Professional system concept: modular fixture + vision + data acquisition + cloud
Fixture bay
HMI unit under test
CAM
Adjustable pins • camera brackets • locating nest • swappable modules
Controller / PLC / SBC
test sequence + timing
DAQ + I/O
voltage, current, bus, inputs
Vision engine
pixel/OCR/icon/flicker checks
Cloud service
dashboards, history, traceability
Output
A single synchronized record: input action, measured electrical state, camera-verified screen state, timing, pass/fail decision, and cloud trace.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
4

## Slide 5
BUSINESS CASE
1. Cost effectiveness: why the static jig has a lower total cost of ownership
Cost category
Static HMI test jig
Robotic hand
Advantage
Mechanical hardware
Extrusion, plates, pins, simple actuators
Dexterous fingers, joints, tendons/gears, wrist/arm
Jig
Controls
PLC/SBC + discrete I/O + camera inputs
Multi-axis motion control + joint feedback loops
Jig
Software
Deterministic test sequence + image checks
Kinematics, path planning, grip/force control
Jig
Calibration
Pin height, camera alignment, reference images
Arm position, hand pose, force, slip, camera
Jig
Service
Swap tips, pins, motors, cameras, panels
Disassemble fingers, encoders, gearboxes, hand
Jig
Operator training
Fixture loading + test start/stop
Robot setup, safety, recovery, programming
Jig
Cost conclusion
The robotic hand pays for dexterity. The HMI test jig pays for repeatable validation. For known screen/button/knob locations, repeatability and data quality produce more value than anthropomorphic motion.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
5

## Slide 6
PLATFORM SCALABILITY
2. Modularity: scalable from small screens to wide cockpit displays
The same base concept can be resized by changing rail length, actuator count, camera positions, and swappable front panels.
small
HMI
medium
screen
large curved / wide dashboard display
Module
Small HMI
Large HMI
Reuse value
Frame rails
short base
extended base
same extrusion ecosystem
Actuator rows
few pins
dense pin rows
same modules
Vision
single camera
multi-camera array
same software
Panels
one plate
multi-zone plates
swappable design
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
6

## Slide 7
MECHANICAL ADVANTAGE
3. Adjustable screw-height pins support curved, sloped, and uneven surfaces
Engineering principle
Instead of solving every surface variation with complex robotic pose control, the jig mechanically conforms each contact point to the HMI geometry during setup.
Cross-section concept
individual screw setting + lock nut
curved / non-flat HMI contact surface
Benefit
What it improves
Why it matters
Robotic hand impact
Height tuning
contact accuracy
same contact point every cycle
requires pose/force control
Lockable setup
repeatability
stable production tests
requires recalibration
Spring/tip options
surface protection
works on glass, buttons, bezels
requires tactile sensing
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
7

## Slide 8
VISION VALIDATION
4. Constant camera feedback: every display state becomes measurable evidence
A robotic hand can press a screen, but it does not prove the HMI responded correctly. Fixed camera feedback closes the loop.
camera-observed display
Frame capture
image timestamp
Registration
align to reference
Analysis
pixel/OCR/icon/flicker
Decision
pass/fail + evidence
Detectable issue
Example
Value
Pixel defects
dead/stuck pixels
quality control
UI failure
wrong icon/text
functional validation
Timing delay
late screen response
performance metric
Flicker/brightness
unstable backlight
reliability signal
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
8

## Slide 9
POWER PROFILE
5. Lower power consumption supports portable and vehicle-powered operation
Reason
A static jig energizes only the pin, rotary module, camera, light, or I/O channel needed for the current test step. A robotic hand must power many joints and may require holding torque plus arm positioning.
Relative power demand profile
idle / waiting
jig
hand
single touch
jig
hand
multi-point test
jig
hand
knob rotation
jig
hand
vehicle endurance
jig
hand
Benefit
Engineering effect
Operational effect
Best use case
smaller supply
less heat/current
portable test kit
field test
battery-friendly
less continuous draw
vehicle cabin use
moving vehicle
less thermal stress
longer component life
better uptime
endurance test
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
9

## Slide 10
MAINTENANCE
6. Serviceability: easy replacement of parts reduces downtime
The static jig should be designed as a maintainable test instrument, not a monolithic robot.
Failure item
Static jig response
Robotic hand response
Downtime risk
worn contact tip
replace rubber/stylus/pogo tip
finger pad or fingertip assembly repair
low vs medium
single actuator
swap press/rotary module
finger joint motor/gear service
low vs high
camera issue
replace fixed camera bracket/module
vision still required separately
low vs medium
connector wear
replace panel connector plate
not primary hand function
low
geometry change
change plate / adjust screws
reprogram pose and recalibrate
low vs high
Inspect
Swap module
Retighten / recalibrate
Run reference test
Return to service
Maintenance objective: minutes to restore operation, not hours of robotic repair and recalibration.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
10

## Slide 11
CONTROL ACTUATION
7. Custom knob-turning modules are more repeatable than robotic gripping
Why dedicated modules win
A knob test needs angle, direction, detent count, torque consistency, and pass/fail correlation—not human-like finger posture. A direct rotary module is mechanically simpler and easier to measure.
Direct coupler
best for exposed shaft / adapter
Friction wheel
best for existing knob surface
Clamp collar
best for repeatable production fixture
Push-turn stack
best for encoder with center push
Measured item
Angle
Detents
Speed
End stop / push
Rotary encoder
yes
yes
yes
optional
Volume/HVAC knob
yes
possible
yes
possible
Selector dial
yes
yes
yes
yes
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
11

## Slide 12
DEPLOYMENT
8–9. Compact, lightweight, and suitable for in-vehicle dynamic testing
The fixture can be built as a compact bench/field system or mounted around an HMI inside a vehicle cabin for real-world validation.
Vehicle cabin mounting concept
HMI
Portability attributes
bench-top footprint
carry-case transport
low vehicle power draw
vibration-tolerant mounting
Real condition
Why it matters
Static jig advantage
Robotic hand issue
vibration/shock
vehicle-representative testing
rigid, low-mass fixture
high inertia
lighting changes
screen readability checks
fixed camera + controlled reference
separate setup
power fluctuation
real ECU/HMI behavior
low draw + logging
large supply demand
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
12

## Slide 13
DATA ARCHITECTURE
10. Real-time data and cloud output turn the jig into a traceable test platform
Test action
pin / knob / button command
Measurement
camera + voltage + bus
Edge decision
limits + timing + evidence
Cloud record
serial, timestamp, result
Dashboard
trends, failures, yield
Data stream
Example fields
Use
Business value
Actuator events
pin ID, force proxy, dwell, knob angle
test reconstruction
root-cause analysis
Vision evidence
image, OCR, icon match, pixel map
screen proof
quality traceability
Electrical data
voltage, current, continuity, bus status
functional proof
reject reduction
Cloud analytics
yield, station, unit serial, failure mode
trend dashboards
process improvement
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
13

## Slide 14
DECISION MATRIX
Weighted scorecard: the jig wins on the criteria that matter most for HMI validation
Criterion
Weight
Static jig
Robotic hand
Reason
Cost effectiveness
high
excellent
poor/fair
jig avoids dexterous hardware and complex motion stack
Repeatability
high
excellent
good
fixed contacts and fixed cameras reduce variation
Curved surface support
high
excellent
fair/good
screw-height pins are direct mechanical compensation
Pixel-level feedback
high
excellent
requires add-on
camera system is native to jig design
Power and portability
medium
excellent
poor/fair
low mass and selective actuation
Maintenance
medium
excellent
fair
modular spares vs specialized robotic repair
Unknown layouts
low/medium
fair
excellent
hand is stronger only when layout is highly variable
Decision rule: choose the robotic hand only if the product requires human-like freeform manipulation. For known HMI layouts, choose the static jig.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
14

## Slide 15
VALIDATION SCOPE
Detailed test coverage enabled by the static HMI jig
Test domain
What the jig does
Evidence captured
Pass/fail example
Touchscreen
presses defined pixel/zone points
camera frames + timing
UI state appears within limit
Physical buttons
linear pin press/release
I/O state + screen response
input toggles, indicator appears
Rotary knobs
turns angle/detents
angle command + UI response
value increments correctly
Push-turn controls
press + rotate sequence
combined action trace
menu navigation correct
Display quality
continuous image capture
pixel/color/OCR/flicker
no dead pixels/wrong icons
Electrical interface
continuity, current, voltage, bus
DAQ + logs
within electrical limits
Cloud reporting
uploads complete result package
traceable record
serial-linked pass/fail
The system validates both the physical interaction and the HMI output, which is the key difference from a simple actuator or robotic hand.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
15

## Slide 16
BUILD QUALITY
Design principles for a professional-grade static HMI test jig
Mechanical
rigid T-slot frame, dowel-located panels, lockable pin height, accessible fasteners
Optical
fixed camera mounts, controlled lighting, calibration target, reference image library
Electrical
fused power, E-stop, isolated I/O, labeled harnesses, terminal blocks, grounding
Software
deterministic sequence, timestamped events, image comparison, retry rules, audit logs
Service
replaceable tips, modular actuator cartridges, panel drawings, spare part kit
Data
local cache, cloud upload, serial traceability, dashboards, failure screenshots
A professional-looking output comes from treating the jig as an industrial test instrument with controlled mechanics, optics, electronics, software, and data.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
16

## Slide 17
BALANCED ASSESSMENT
Risk register and mitigation plan
Risk / limitation
Severity
Mitigation
Residual impact
Product layout changes
medium
use modular plates, movable rails, stored calibration templates
manageable
Very complex gestures
medium
add specialized swipe/drag/rotary modules only where needed
localized design work
Camera occlusion
medium
use multi-camera angles, lighting control, clear pin placement
manageable
Pin wear or surface marks
low/medium
use replaceable soft tips, force limits, inspection schedule
low
Cloud connectivity loss
low/medium
local cache and delayed upload
low
Initial fixture setup time
medium
document calibration workflow and reusable templates
low after first setup
Balanced conclusion: the jig is not a universal manipulator, but it is the stronger engineering choice for known HMI validation targets.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
17

## Slide 18
VALUE CASE
Business value: where the static jig creates measurable advantage
Lower capital spend
fewer specialized robotic components
Lower operating cost
less power, simpler spares, less downtime
Higher throughput
parallel contacts and deterministic sequences
Better quality evidence
camera screenshots and pixel-level checks
Faster product adaptation
modular panels and adjustable pins
Field/vehicle readiness
compact, light, and low power
Improved traceability
cloud records linked to unit serial numbers
Reduced training burden
fixture operation instead of robot programming
The static jig is not just cheaper hardware; it is a better test economics model for repeatable HMI validation.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
18

## Slide 19
CONCLUSION
Final recommendation
Choose the static Robo HMI test jig as the primary platform for HMI screen, button, knob, and dashboard validation.
Why it is more effective
Why it is more versatile
Why it is more cost-effective
fixed geometry gives repeatable contacts
modular frame supports small/large screens
commodity parts replace expensive dexterity
camera feedback verifies the actual HMI output
screw-adjustable pins handle curved surfaces
lower maintenance and calibration burden
cloud logs create traceable evidence
knob/button/touch modules can be swapped
lower power and smaller deployment footprint
better suited to in-vehicle real-world tests
portable enough for lab, field, and vehicle use
faster repair with simple spare parts
Use a robotic hand only when the requirement is truly human-like manipulation of unknown objects. For known HMI layouts, the static jig is the more practical, scalable, and defensible engineering solution.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
19

## Slide 20
PRESENTER NOTES
Appendix: slide-by-slide narrative for presenting the deck
Slide
Purpose
Presenter message
1–3
Frame the decision
The objective is not to imitate a hand; it is to validate HMI behavior with repeatability and evidence.
4
Explain architecture
The jig combines mechanical actuation, cameras, electrical I/O, and cloud reporting.
5
Defend cost
Robotic hand cost is driven by dexterity that adds little value to fixed HMI tests.
6–8
Show technical advantages
Modularity, adjustable pins, and cameras solve real HMI problems directly.
9–13
Show operations
Low power, serviceability, portability, and cloud data improve daily usability.
14–18
Make the business case
Decision matrix, coverage, risks, and business value support the recommendation.
19
Close
Recommend the static jig as the primary platform and reserve robotic hands for true dexterity use cases.
Static Robo HMI Test Jig vs. Robotic Hand | Research Deck
20